## Slide 1: Spanning Tree Protocol (STP)
Loop Prevention in Layer 2 Networks

## Slide 2: Basic Communication in Networks
Devices need MAC address
Broadcast request (ARP)
Switch forwards to all devices

## Slide 3: Broadcast in Simple Network
Single switch
Controlled broadcast
Normal communication

## Slide 4: Problem in Multi-Switch Network
Multiple switches
Broadcast loops
Infinite circulation

## Slide 5: Broadcast Loop Issue
Broadcast storm
Network congestion
MAC instability

## Slide 6: How STP Solves It
Blocks certain ports
Creates loop-free topology

## Slide 7: Root Bridge Selection
Switches exchange BPDUs
Elect root bridge

## Slide 8: Bridge ID (BID)
Priority + VLAN + MAC
Default: 32768 + VLAN

## Slide 9: Root Bridge Election
Lowest BID wins
If same → lowest MAC

## Slide 10: Designated Ports
On root bridge
Always forwarding

## Slide 11: Root Ports
On non-root switches
Lowest path cost

## Slide 12: Path Cost
1Gbps=4
100Mbps=19
10Mbps=100

## Slide 13: Blocked Ports
Higher cost or BID
Prevent loops

## Slide 14: Final Result
Loop-free network
Active + backup paths

## Slide 15: Conclusion
STP prevents loops
Uses BPDUs
Ensures stability

## Slide 16: Security Perspective
BPDU spoofing
Attacker becomes root
MITM risk